mWAVE Antenna Test: 07/02/2019

Equipment:
- SG6000LDQ signal generator
- Anker battery pack
- 2 SMA cables (1 referred to as blue (long) and the other blue (short)
- 2 mWAVE dish antennas (22.5 – 27.5 GHz range)
- 2 tripod stands
- Spectrum Analyzer (Anritsu MS2720T)

Description:
Two mWAVE dish antennas were mounted on separate tripod stands and placed a set distance apart. A signal was transmitted from one of the antennas using a signal generator. The second antenna was wired to a spectrum analyzer to record the data.

Results:
- Frequency: 22.0 GHz
- Signal generator input power: 12.8 dBm
- Distance: 172.5 inches (14’ 4.5”)
- SMA cable blue(long) loss: 3.38 dBm
- SMA cable blue(short) loss: 1.66 dBm
- Free space path loss: 65.21 dBm
- Rx channel power: -10.8 dBm
- Calculated antenna gain: ≈ 23 dBm